## Slide 1
RTP Sink
(Nexx WT3050)
MIC Source (Nexx WT3050)
MIC Source
(Nexx WT3050)
GA LXC
GA LXC
Central Audio Mixer
Multicast RTP
Source Tunnel
Source Tunnel
RTP Sink
(Nexx WT3050)
ALSA pulse plugin (GA does not natively support PulseAudio)
Currently, this is one large RTP multicast channel, however in the near future, this will be implemented as multiple multicast RTP channels representing zones which can be turned on and off.
Multiple Google Assistant (and Alexa,
and MyCroft AI) containers, one per zone, for 2 reasons – 1, clearer audio when not combining multiple audio inputs and 2, future context awareness eg “turn on tv” will turn on local TV only.
Local Input (eg. TV)
Local Input (eg. TV)
MaryTTS
Text-to-speech
MPD
Google Play Music
Lounge
Bedroom
Sink Tunnel
Sink Tunnel